## Slide 1
402084 DIGITAL IMAGE PROCESSING
CHAPTER 1: DIGITAL IMAGE PROCESSING INTRODUCTION
Vu Anh. Le, Phd.
TON DUC THANG UNIVERSITY
FACULTY OF ELECTRICAL AND ELECTRONICS ENGINEERING

## Slide 2: OBJECTIVES
Known properties of the digital image
Know the digital image sensor and digital image acquisition.
Understand the light characteristics and human visual system
Understand the way to represent a digital image and color space.

## Slide 3: CHAPTER 1: Digital image processing introduction
1.1 INTRODUCTION ABOUT DIGITAL IMAGE PROCESSING
1.2 CAMERA AND HUMAN VISUAL SYSTEM
1.3 REPRESENT A DIGITAL IMAGE AND COLOR SPACE

## Slide 4: Introduction about Digital Image Processing
A continuous image is 2D function
1D: f(t) is a function f that depends on time t.
2D: f(x,y) is a function f that depends on the spatial (room) coordinates x and y.

## Slide 5: Introduction about Digital Image Processing
Ex)

## Slide 6: Introduction about Digital Image Processing
An example of a digital image

## Slide 7: Application of Digital Image Processing
Goal of computer vision is to write computer programs that can interpret images
Can computers match (or beat)
human vision?
Yes and no (but mostly no!)
  humans are much better at “hard” things
  computers can be better at “easy” things

## Slide 8: Application of Digital Image Processing
Optical character recognition (OCR)
  Technology to convert scanned docs to text
License plate readers
http://en.wikipedia.org/wiki/Automatic_number_plate_recognition

## Slide 9: Application of Digital Image Processing
Face detection
  Many new digital cameras now detect faces Canon, Sony, Fuji, …

## Slide 10: Application of Digital Image Processing
Sony Cyber-shot® T70 Digital Still Camera
Smile detection

## Slide 11: Application of Digital Image Processing
Who is she?
Face recognition
“How the Afghan Girl was Identified by Her Iris Patterns”

## Slide 12: Application of Digital Image Processing
Earth viewers (3D modeling)

## Slide 13: Application of Digital Image Processing
Login without a password
Fingerprint scanners on many new laptops, other devices
Face recognition systems now beginning to appear more widely http://www.sensiblevision.com/

## Slide 14: Application of Digital Image Processing
This is becoming real:
  Microsoft Research
  Point & Find, Nokia
Object recognition (in mobile phones)

## Slide 15: Application of Digital Image Processing
Special effects: shape capture

## Slide 16: Application of Digital Image Processing
Special effects: motion capture

## Slide 17: Application of Digital Image Processing
Sports analyse
Sport vision first down line

## Slide 18: Application of Digital Image Processing
Smart cars
  Vision systems currently in high-end BMW, GM, By 2010: 70% of car manufacturers.
Object recognition (in mobile phones)

## Slide 19: Application of Digital Image Processing
Digimask: put your face on a 3D avatar.
“Game turns moviegoers into Human Joysticks”
Vision-based interaction (and games)

## Slide 20: Application of Digital Image Processing
NASA'S Mars Exploration Rover Spirit captured this westward view from atop a low plateau where Spirit spent the closing months of 2007.
Vision in space
  Panorama stitching, 3D terrain modeling
  Obstacle detection, position tracking

## Slide 21: Application of Digital Image Processing
3D imaging
MRI, CT
Medical Image

## Slide 22: Application of Digital Image Processing
http://www.robocup.org/
NASA’s Mars Spirit Rover
http://en.wikipedia.org/wiki/Spirit_rover
Robotics

## Slide 23: Basic steps in Digital Image Processing

## Slide 24: CHAPTER 1: Digital image processing introduction
1.1 INTRODUCTION ABOUT DIGITAL IMAGE PROCESSING
1.2 CAMERA AND HUMAN VISUAL SYSTEM
1.3 REPRESENT A DIGITAL IMAGE AND COLOR SPACE

## Slide 25: Camera and Human Perception System
Digital Image Sensor

## Slide 26: Camera and Human Perception System
Digital Image Acquisition Process
  Capture real object to image

## Slide 27: Camera and Human Perception System
Digital Image Acquisition Process
  Sampling and quantization

## Slide 28: Camera and Human Perception System
Results of sampling and quantization

## Slide 29: Camera and Human Perception System
Digital Image Acquisition Process
  represent an image in 3D and 2 D

## Slide 30: Camera and Human Perception System
Spatial resolution

## Slide 31: Camera and Human Perception System
  gray scale images 8 bits per pixels, i.e. 2 8 =256 intensity levels.
  Color images are usually stored with 3x8 bits per pixels,
  2^8 red intensity levels, 2^8 green intensity levels and 2^8 blue intensity levels.
Intensity resolution

## Slide 32: Camera and Human Perception System
Intensity Resolution
  Present by power of 2. ex) 2^8= 256 values form 0-255
  More bits more detail

## Slide 33: Camera and Human Perception System
Gray scale image compared to true color image

## Slide 34: Camera and Human Perception System
The electromagnetic spectrum
  Wavelength of difference source

## Slide 35: Camera and Human Perception System
The electromagnetic spectrum
  Examples of different images from different sources

## Slide 36: Camera and Human Perception System
The electromagnetic spectrum
  Examples of different images from different sources

## Slide 37: Camera and Human Perception System
Examples of different images from different sources

## Slide 38: Camera and Human Perception System
Human Visual system
  The human eye contains 3 types of sensors named cones, sensible to blue, green and red light, respectively.
  The human eye regards a color as a combination of 3 primary colors blue (B), green (G) and red (R).

## Slide 39: Camera and Human Perception System
Human Visual system
  Basically, the eye works much like a camera

## Slide 40: CHAPTER 1: Digital image processing introduction
1.1 INTRODUCTION ABOUT DIGITAL IMAGE PROCESSING
1.2 CAMERA AND HUMAN VISUAL SYSTEM
1.3 REPRESENT A DIGITAL IMAGE AND COLOR SPACE

## Slide 41: The Methods to represent Digital color image
The colors perceive in an object are determined by the nature of the light reflected from the object
  E.g: green objects of 500 – 570 nm while absorbing most of the energy at other wavelengths
White Light
colors Absorbed
Green Light

## Slide 42: The Methods to represent Digital color image
Wavelength of the light

## Slide 43: The Methods to represent Digital color image
3 basic qualities of a chromatic light source:
  Radiance: the total amount of energy that flows from the light source (measured in watts)
  Luminance: the amount of energy an observer perceives from the light source (measured in lumens)
  Brightness: a subjective (practically unmeasurable) notion that embodies the intensity of light

## Slide 44: The Methods to represent Digital color image
CIE 1931 XYZ system
  One of the color spaces
  The first mathematical defined color space
  Three parameter:
  X, Y, Z
  or Y (brightness), x, y (chroma)

## Slide 45: The Methods to represent Digital color image
CIE
  Chromaticity Diagram
  Spectral Locus
  Parameter x, y

## Slide 46: The Methods to represent Digital color image

## Slide 47: The Methods to represent Digital color image
The CIE System
  Y: the brightness
  The Chroma parameter x, y :

## Slide 48
This means the entire color range cannot be displayed based on any three colors
The triangle shows the typical color gamut produced by RGB monitors
The strange shape is the gamut achieved by high quality color printers
CIE Chromacity Diagram
The Methods to represent Digital color image

## Slide 49: The Methods to represent Digital color image
Color Space: What is color space?
  A 3D model used to define a specified color
The difference between color spaces:
  The choice of axes

## Slide 50
Two very popular models used in color image processing:
  RGB (Red Green Blue)
  HIS (Hue Saturation Intensity)
The Methods to represent Digital color image

## Slide 51
The Methods to represent Digital color image
RGB modle
  Consist of three component images – one for each primary color
  When fed into a monitor these images are combined to create a composite color image
  The number of bits used to represent each pixel is referred to as the color depth
  E.g: A 24-bit image is often referred to as a full-color image as it allows 16,777,216 colors

## Slide 52
The Methods to represent Digital color image
RGB modle

## Slide 53: The Methods to represent Digital color image
Color Space:
  RGB
  YCbCr (YPbPr)
  YUV
  YIQ
  CMYK

## Slide 54: The Methods to represent Digital color image
YCbCr & YPbPr
  Used for: digital video encoding, digital camera
Axes:
  Y: luma
  Cb: blue chroma
  Cr: red chroma

## Slide 55: The Methods to represent Digital color image
Conversion from RGB:
  Y=0.299(R-G) + G + 0.114(B-G)
  Cb=0.564(B-Y)
  Cr=0.713(R-Y)
The Matrix form:

## Slide 56: The Methods to represent Digital color image
YUV
  Used for: video encoding for some standard such as NTSC, PAL, SECAM
Axes:
  Y: luma
  U: blue chroma
  V: red chroma

## Slide 57: The Methods to represent Digital color image
Conversion from RGB:
  Y=0.299R+0.587G+0.114B
  U=0.436(B-Y)/(1-0.114)
  V=0.615(R-Y)/(1-0.299)
The Matrix form:

## Slide 58: represent a digital image and color space
The HSI color model
  The HSI (Hue,(Hue, Saturation, Intensity)
  Decouples thee intensity information from the color-carrying information.
  Is good for describing monochromatic images

## Slide 59: represent a digital image and color space
Hue (H) and saturation (S) the HSI model
  good for describing colors

## Slide 60: represent a digital image and color space
Color space | Color mixing | Primary parameters | Used for | Pros and cons
RGB | Additive | Red, Green, Blue |  | Easy but wasting bandwidth
CMYK | Subtractive | Cyan, Magenta, Yellow, Black | Printer | Works in pigment mixing
YCbCr YPbPr | additive | Y(luminance), Cb(blue chroma), Cr(red chroma) | Video encoding, digital camera | Bandwidth efficient
YUV | additive | Y(luminance), U(blue chroma), V(red chroma) | Video encoding for NTSC, PAL, SECAM | Bandwidth efficient
YIQ | additive | Y(luminance), I(rotated from U), Q(rotated from V) | Video encoding for NTSC | Bandwidth efficient

## Slide 61: SUMMARY
This chapter we have learnt:
  Define digital image .
  Define basic digital image processing steps.
  Digital image sensor and acquisition.
  Color space models .

## Slide 62: HOMEWORK
Review the chapter 1
Read chapter 2 : 23-65, 417-436
Reference [2]: 13-49
Solve the exercise: 2.1, 2.2, 2.4, 2.5, 2.7, 2.11, 2.12, 2.15, 2.20, 2.62.