## Slide 1
402084 DIGITAL IMAGE PROCESSING
CHAPTER 3: DIGITAL IMAGE COMPRESION
Vu Anh. Le, Phd.
TON DUC THANG UNIVERSITY
FACULTY OF ELECTRICAL AND ELECTRONICS ENGINEERING

## Slide 2: OBJECTIVES
Known why need image compression
Know the block diagram of image compression .
Understand Huffman coding, lossless and lossy coding
Understand JPEG image conpression standard.

## Slide 3: CHAPTER 3: Digital image compression
1.1 IMAGE COMPRESSION OVERVIEW
1.2 DITGITAL IMAGE COMPRESSION STEPS
1.3 HUFFMAN CODING
1.4 JPEG STANDARD

## Slide 4: IMAGE COMPRESSION OVERVIEW
The size of typical still image (1200x1600)
The size of two hours standard television (720x480) movies

## Slide 5: IMAGE COMPRESSION OVERVIEW
Data, Information, and Redundancy
  The term data compression refers to the process of reducing the amount of data required to represent a given quantity of information
  Data is used to represent Information
  Redundancy in data representation of an information provides no relevant information or repeats a stated information

## Slide 6: IMAGE COMPRESSION OVERVIEW
Data, Information, and Redundancy
  Let n1 and n2 denote the number of information carrying units in two data sets that represent the same information
  The relative redundancy RD is define as :
  where CR, commonly called the compression ratio, is

## Slide 7: IMAGE COMPRESSION OVERVIEW
Data, Information, and Redundancy
  If n1 = n2 , CR=1 and RD=0 no redundancy
  If n1 >> n2 , CR and RD high redundancy
  If n1 << n2 , CR and RD undesirable
  A compression ration of 10 (10:1) means that the first data set has 10 information carrying units (say, bits) for every 1 unit in the second (compressed) data set.

## Slide 8: IMAGE COMPRESSION OVERVIEW
Redundancy in Digital Images Data
  Coding redundancy: usually appear as results of the uniform representation of each pixel
  Inter-pixel Redundancy : because the adjacent pixels tend to have similarity in practical.
  Irrelevant Information: Image contain information which are ignored by the human visual system.

## Slide 9: IMAGE COMPRESSION OVERVIEW
Coding Redundancy
  Recall from the histogram calculations
  The average code bits length assigned to the gray level values.
  The length of the code should be inverse proportional to its probability (occurrence).

## Slide 10: IMAGE COMPRESSION OVERVIEW
Coding Redundancy
  Example

## Slide 11: IMAGE COMPRESSION OVERVIEW
Coding Redundancy
Variable-Length
Coding

## Slide 12: IMAGE COMPRESSION OVERVIEW
Inter-pixel Redundancy
  Internal Correlation between the pixel
  A pixel can be predicted from the values of its neighbors.
  To reduce 2D array is transformed (mapped) into more efficient format (Frequency Domain etc.)

## Slide 13: IMAGE COMPRESSION OVERVIEW
Run-Length Encoding
  Example of Inter-pixel Redundancy removal

## Slide 14: IMAGE COMPRESSION OVERVIEW
Irrelevant information and Psycho-Visual Redundancy Internal Correlation between the pixel
  The perceived intensity of the eye is limited
  Certain information has less relative importance that other information in normal visual processing
  In general, observer searches for distinguishing features such as edges and textural regions

## Slide 15: IMAGE COMPRESSION OVERVIEW
The human visual system is more sensitive to edges
Middle Picture:
  Uniform quantization from 256 to
  16 gray levels
  CR= 2
Right picture:
  Improved gray level quantization
  (IGS)
  CR= 2
  The perceived intensity of the eye is limited
  Certain information has less relative importance that other information in normal visual processing
  In general, observer searches for distinguishing features such as edges and textural regions

## Slide 16: IMAGE COMPRESSION OVERVIEW
Measuring Information
  A random even E that occurs with probability P(E) is said to contain I(E) information where I(E) is defined as

## Slide 17: IMAGE COMPRESSION OVERVIEW
Measuring Information
  For a source of events a0 , a1 ,a2 , .., ak with associated probability
  For image, we use the normalized histogram to generate the source probability, which leads to the entropy

## Slide 18: IMAGE COMPRESSION OVERVIEW
Fidelity Criteria-Objective Fidelity Criteria

## Slide 19: IMAGE COMPRESSION OVERVIEW
Fidelity Criteria-Objective Fidelity Criteria

## Slide 20: IMAGE COMPRESSION OVERVIEW
Fidelity Criteria-Objective Fidelity Criteria

## Slide 21: CHAPTER 3: Digital image compression
1.1 IMAGE COMPRESSION OVERVIEW
1.2 DITGITAL IMAGE COMPRESSION STEPS
1.3 HUFFMAN CODING
1.4 JPEG STANDARD

## Slide 22: Digital image compression steps
Compression Model
  The source encoder is responsible for removing redundancy (coding, inter-pixel, psycho-visual)
  The channel encoder ensures robustness against channel noise

## Slide 23: Digital image compression steps
Compression Types
Compression
Error-Free Compression
(Loss-less)
Lossy Compression

## Slide 24: Digital image compression steps
Error-Free Compression
  Some applications require no error in compression (medical, business documents, etc..)
  CR=2 to 10 can be expected.
  Make use of coding redundancy and inter-pixel redundancy.
  Ex: Huffman codes, LZW, Arithmetic coding, 1D and 2D run-length encoding, Loss-less Predictive Coding, and Bit-Plane Coding.

## Slide 25: Digital image compression steps
Image/Video Compression Standards

## Slide 26: Digital image compression steps
Huffman coding
  An entropy encoding algorithm used for lossless data compression.
  The term refers to the use of a variable length code table for encoding a source symbol
  The variable-length code table has been derived in a particular way based on the estimated probability of occurrence for each possible value of the source symbol

## Slide 27: Digital image compression steps
Huffman coding

## Slide 28: Digital image compression steps
Fixed Length: LZW
  Error Free Compression Technique
  Remove Inter-pixel redundancy
  Requires no priori knowledge of probability distribution of pixels
  Assigns fixed length code words to variable length sequences
  Included in GIF and TIFF and PDF file formats

## Slide 29: Digital image compression steps
Fixed Length: LZW Coding Technique
  A codebook or a dictionary has to be constructed
  For an 8-bit monochrome image, the first 256 entries are assigned to the gray levels 0,1,2,..,255.
  As the encoder examines image pixels, gray level sequences that are not in the dictionary are assigned to a new entry.

## Slide 30: Digital image compression steps
Fixed Length: LZW
Example
Consider the following 4 x 4 8 bit image
39 39 126 126
39 39 126 126
39 39 126 126
39 39 126 126
Dictionary Location Entry
0 0
1 1
. .
255 255
256 -
511 -
Initial Dictionary

## Slide 31: Digital image compression steps
Fixed Length: LZW
39 39 126 126
39 39 126 126
39 39 126 126
39 39 126 126
Is 39 in the dictionary……..Yes
What about 39-39………….No
Then add 39-39 in entry 256
And output the last recognized symbol…39x
Dictionary Location Entry
0 0
1 1
. .
255 255
256 -
511 -
39-39

## Slide 32: Digital image compression steps
Fixed Length: LZW
Code the following image using LZW codes
39 39 126 126
39 39 126 126
39 39 126 126
39 39 126 126
* How can we decode the compressed sequence to obtain the original image ?

## Slide 33: Digital image compression steps
Fixed Length: LZW

## Slide 34: Digital image compression steps
Loss-less Predictive Encoding

## Slide 35: Digital image compression steps
Loss-less Predictive Encoding
  For each pixel a predictor (one of 7 possible) is used that best predicts the value contained in the pixel as a combination of up to 3 neighboring pixels.
  The difference between the predicted value and the actual value (X) contained in the pixel is used as the predictive difference to represent the pixel.
  The predictor along with the predictive difference are encoded as the pixel’s content.
  The series of pixel values are encoded using Huffman coding

## Slide 36: Digital image compression steps
Loss-less Predictive Encoding
C
B
A
X
Predictor | Prediction
P1 | A
P2 | B
P3 | C
P4 | A+B-C
P5 | A + (B-C)/2
P6 | B + (A-C)/2
P7 | (A+B)/2
Notes:
The very first pixel in location (0, 0) will always use itself.
Pixels at the first row always use P1,
Pixels at the first column always use P2.
The best (of the 7) predictions is always chosen for any pixel.

## Slide 37: Digital image compression steps
Lossy Compression
Quantizer

## Slide 38: Digital image compression steps
Transform Coding
  Decorrelate pixels and pack as much information into small number of transform coefficients.
  A reversible linear transform (such as Fourier Transform) is used to map the image into a set of transform coefficients
  These coefficients are then quantized and coded.
  Compression is achieved during quantization not during the transform step

## Slide 39: Digital image compression steps
Transform Coding block diagram

## Slide 40: Digital image compression steps
2D Transforms
  Energy packing: 2D transforms pack most of the energy into small number of coefficients located
  at the upper left corner of the 2D array
Energy
Packing

## Slide 41: Digital image compression steps
2D Transforms
  Consider an image f(x,y) of size N x N
  Forward transform
  g(x,y,u,v) is the forward transformation kernel or basis functions

## Slide 42: Digital image compression steps
2D Transforms
  Consider an image f(x,y) of size N x N
  Inverse transform
h(x,y,u,v) is the inverse transformation kernel or basis functions

## Slide 43: Digital image compression steps
Discrete Cosine Transform
  One of the most frequently used transformations for image compression is the DCT.
  Consider an image f(x,y) of size N x N

## Slide 44: Digital image compression steps
Discrete Cosine Transform
  Consider an image f(x,y) of size N x N
  Coefficients of DCT: note the DC and AC components of difference frequencies

## Slide 45: Digital image compression steps
Discrete Cosine Transform
  Effect of Window Size

## Slide 46: Digital image compression steps
Discrete Cosine Transform
  Compare DCT an FFT
46
100 | -52 | 0 | -5 | 0 | -2 | 0 | 0.4
36 | 10 | 10 | 6 | 6 | 4 | 4 | 4
36 | 10 | 10 | 6 | 6 | 4 | 4 | 4
100 | -52 | 0 | -5 | 0 | -2 | 0 | 0.4
24 | 12 | 20 | 32 | 40 | 51 | 59 | 48
8 | 15 | 24 | 32 | 40 | 48 | 57 | 63
DCT
FFT
Inverse DCT
Inverse FFT

## Slide 47: Digital image compression steps
Quantization: reduce number of bits per sample
Quantization error is the main source of the Lossy Compression.
Uniform Quantization: q(u,v) is a constant
Non-uniform Quantization -- Quantization Tables
  Eye is most sensitive to low frequencies (upper left corner in frequency matrix)
  less sensitive to high frequencies (lower right corner)
Quantizer

## Slide 48: Digital image compression steps
Quantization: reduce number of bits per sample
Each transformed coefficient is quantized
  Z(u,v) quantization coefficients
Quantizer

## Slide 49: Digital image compression steps
Bit allocation and Zig Zag Ordering
  to group low frequency coefficients in top of vector and high frequency coefficients at the bottom
  Maps 8 x 8 matrix to a 1 x 64 vector
8x8
. . .
1x64

## Slide 50: Digital image compression steps
DPCM on DC Components
  The DC component often close to that in the previous block
  Differential Pulse Code Modulation (DPCM): Remember, smaller number -> fewer bits
45
54
48
45
9
-6
1x64
1x64
1x64
1x64
1x64
1x64

## Slide 51: Digital image compression steps
RLE on AC Components
  The 1x64 vectors have a lot of zeros in them, more so towards the end of the vector
  Encode a series of 0s as a (skip, value) pair
. . .
1x64
0
0
0
0
0
1
1
0
0
0
0
0
0
0
0
. . .
2

## Slide 52: Digital image compression steps
DCT and Quantization
Right Column

## Slide 53: CHAPTER 3: Digital image compression
1.1 IMAGE COMPRESSION OVERVIEW
1.2 DITGITAL IMAGE COMPRESSION STEPS
1.3 HUFFMAN CODING
1.4 JPEG STANDARD

## Slide 54: HUFFMAN CODING
Coding Redundancy
  Example

## Slide 55: HUFFMAN CODING
Coding Redundancy
Variable-Length
Coding

## Slide 56: CHAPTER 3: Digital image compression
1.1 IMAGE COMPRESSION OVERVIEW
1.2 DITGITAL IMAGE COMPRESSION STEPS
1.3 HUFFMAN CODING
1.4 JPEG STANDARD

## Slide 57: JPEG STANDARD
JPEG Compression
  DCT
  Quantization
  Zig-Zag Scan
  RLE and DPCM
  Entropy Coding

## Slide 58: JPEG STANDARD
58
Y
Cb
Cr
DPCM
RLC
Entropy
Coding
Header
Tables
Data
Coding
Tables
Quant…
Tables
DCT
f(i, j)
8 x 8
F(u, v)
8 x 8
Quantization
Fq(u, v)
Zig Zag
Scan
Block diagram

## Slide 59: JPEG STANDARD
59
Steps Involved:
  Discrete Cosine Transform of each 8x8 pixel array f(x,y) T F(u,v)
  Quantization using a table or using a constant
  Zig-Zag scan to exploit redundancy
  Differential Pulse Code Modulation(DPCM) on the DC component and Run length Coding of the AC components
  Entropy coding (Huffman) of the final output

## Slide 60: SUMMARY
This chapter we have learnt:
  The need image compression
  block diagram of image compression .
  Huffman coding, lossless and lossy coding
  JPEG image conpression standard.

## Slide 61: HOMEWORK
Review the Chapter 3
Read chapter 4 (pp. 547-564 )
Solve the exercise: 3.1, 3.2, 3.4, 3.5, 3.7, 3.11, 3.12, 3.15, 3.20, 3.25.